F9/AS2 (Covers for small heated pools)

Most building work requires a building consent and the construction of a residential pool barrier is building work. Building work not requiring a building consent is listed in Schedule 1 of the Building Act, Clause 21A of Schedule 1 now includes:
Installation of a safety cover as a means of restricting access to a small heated pool that is a residential pool.
South Pacific Covers as manufacturer and distributor confirms that, with respect to its Lockable Spa Cover, all the requirements of F9/AS2 are complied with. The only other requirements are those that the spa owner / property owner must meet. All these are set out below. Property owners may use this information should any other consent be required from Council.
The Spa Pool is manufactured to a minimum height of 760mm. It is designed to be set down on a firm flat
surface and not set into the ground or a deck. The cross section of the cover shows the insulating
foam billets fitted with the rigid E bar for strength with Six evenly spaced lockable catches fitted.

The cover is:
1: Manufactured with a commercial grade vinyl and UVR thread that meets ASTM F1346-91;
2: Tapered from the centre line to the outside, 90mm to 40mm, to allow water runoff;
3: Strengthened by the addition of rigid E bars to the foam billets at the centre fold point;
4: Capable of holding a 20Kg weight;
5: Fitted with six evenly spaced lockable catches that may be locked with the supplied key;
6: Not able to be lifted, once latched, to give a clearance of 100mm, and
7: Stamped with the words WARNING “This cover must be kept locked except when under adult supervision” together with the approved warning logo on the handle.

South Pacific Covers:
1: Believe that a child aged under six will not be able to open the catches once locked;
2: Believe that a cover properly maintained will have a life of at least five years;
3: Recommend that persons do not jump or sit on the cover;
4: Recommend that the cover is cleaned twice yearly with a vinyl cleaner that does not contain petroleum solvents and that the lockable catches are washed twice yearly.

The property owner is responsible to ensure that:
1: The spa pool is set down in such a way that a minimum height of 760mm is maintained at all points;
2: Removable steps or objects that may allow a child to climb up, are stowed at least further then a minimum radius of 1.2m from the top lip of the spa;
3: When the pool is not in use or supervised the cover will be kept locked;
4: The cover and lockable catches are maintained in a good working order, and
5: At all times the provisions of NZS 8500:2006 are met.